## Slide 1
EPICS 7 – Introduction and Overview Ralph Lange

## Slide 2
Outline
Creation
  Initial goals of the EPICS 7 project
  The pvAccess protocol
Evolution
  Normative Types
  Integration in the EPICS context
  Use cases for the new protocol
  Increased adoption in the community
Plans
  IPv6 support
  TLS security on the network

## Slide 3
Creation
EPICS 7 and its Initial Goals

## Slide 4
Initial Goals (2007)
Leave no lab behind
“EPICS V4” Group could not agree on basic design ideas for “perfect” IOC
New user-focused goals:
Don’t break the IOC (Input/Output Controller) software
Extend the scope, allowing migration for existing installations
Provide a migration path with minimal configuration
Include user-level libraries for Java, C++, Python
3 + 4 = 7

## Slide 5
The pvAccess (PVA) Protocol
Transporting arbitrary structures efficiently
Based on a reasonable set of standard types and arrays, plus structures of those, plus variants
Similar to Channel Access in many aspects
  Client needs to know the name, not the server
Subscriptions are very efficient
  On opening a subscription, the client gets a full structure copy
  Any further updates only contain the elements that have changed
  The client has a consistent full copy at any time
New “RPC” Access method
  “Argument” (structure) posted with the call
  “Return value” (structure) may differ in type between calls

## Slide 6
Evolution
The Last Years

## Slide 7
Normative Types (NT)
Arbitrary structures can be a bad idea
Normative Types define standard structures for standard use cases
  All fixed structure types of Channel Access are covered
  Plus: 2D array, table, image (+ metadata), time series, channel collection, …
Generic clients (e.g., GUI, Archivers, services) understand NTs
Specific types, however, are possible and common
  Support by generic clients is very limited (often reduced to printing)
  Applications become specific and non-portable
Use Normative Types whenever possible and reasonable

## Slide 8
Integration
Fitting in with the others
In the IOC (QSRV):
PVA server allows access to all records.fields using Normative Types
Multiple record.fields can be configured into an arbitrary structure
In clients, like GUI frameworks and archivers:
In Phoebus, channel names are prefixed with “ca://” or “pva://” with a configurable default
The Databrowser always searches on both protocols to provide consistent data across migration

## Slide 9
Use Cases
Things that were not possible before
Images: An image Normative Type contains image and metadata in a single structure; clients always have a consistent set
Middle-layer services: The RPC-type method (request/response with changing payload) allows wrapping database, model or directory service calls
Transactional configuration: Using the RPC type method, a client can write configuration for a complete subsystem in a single structure

## Slide 10
Adoption
Important new and upgrade projects have selected EPICS 7
New installations can start using pvAccess
There’s a smooth migration path for existing installations
User-level libraries:
Second generation libraries make better use of language specifics core-pva (Java), PVXS (C++)
Real-time for legacy VME:
RTEMS is well supported in EPICS 7

## Slide 11
Plans
Current Projects

## Slide 12
IPv6
The second generation user-level libraries support IPv6
Security
At SLAC, a multi-year project is underway that will add industrial-level security TLS-style security to the pvAccess protocol
Secure communication itself is working
The hard part, i.e. key management, has a working prototype

## Slide 13
Conclusions

## Slide 14
Conclusions
All initial goals of the development have been met
The migration path works: we see increasing adoption and use
Users are beginning to explore the new possibilities
Future challenges are being addressed
Of course, there is still room for improvement
Questions?